## Slide 1: High-performance Branch Predictors For Soft Processors
Di Wu
M.A.Sc Defense
September 8, 2014

## Slide 2: Why Branch Prediction
Fetch and execute speculatively
Without a Branch Predictor
stall
Branch Predictor: Correct prediction
Fetch and execute speculatively
Branch Predictor: Incorrect prediction
Branch resolved
Squash
Guess Next PC
Guess Next PC
Branch
Time

## Slide 3: Branch Predictors on FPGAs
iCache
(BRAM)
Branch Prediction Table
(BRAM)
Branch Prediction Logic
Fetch Stage
Decode Stage
Next PC
Faster relative to ASIC
Slower relative to ASIC

## Slide 4: Road Map
Introduction
Branch Prediction Overview
Branch Target Predictors
Branch Direction Predictors
Conclusion

## Slide 5: Branch Prediction
iCache
Branch Prediction
Table
Branch Prediction Logic
Fetch Stage
Decode Stage
Next PC
REQ1: Guess the direction of a branch
REQ2: Guess its target (Next PC)
Fetch instructions from there
Execute Speculatively
Verify if the prediction was correct

## Slide 6: REQ #1. Direction Predictors
PC
…
bimodal
PC
…
gshare
GHR
XOR
PC
…
gselect
Concatenate
DIR table
DIR table
DIR table
GHR

## Slide 7: Direction Predictors - Perceptron
weight vector
Weight Table
w0
X
G0
wh
X
Gh
……
+

## Slide 8: Direction Predictors - TAGE
base
T0
ctr
tag
u
hash
T1
hash
PC
=?
PC
h[0:L(1)]
ctr
tag
u
hash
T2
hash
PC
=?
h[0:L(2)]
ctr
tag
u
hash
T3
hash
PC
=?
h[0:L(3)]
ctr
tag
u
hash
T4
hash
PC
=?
h[0:L(4)]
Prediction

## Slide 9: REQ #2: Target Predictor
Branch Target Buffer (BTB)
  Can be used for all branches
Return Address Stack (RAS)
  Uses calls to predict targets of returns
Target Address Pre-calculation

## Slide 10: Canonical Branch Predictor
PC
BTB
+4
PC + 4
DIR
Next PC
RAS
Selection Logic

## Slide 11: Road Map
Introduction
Branch Prediction Overview
Branch Target Predictors
Branch Direction Predictors
Conclusion

## Slide 12: Target Address Pre-calculation
iCache
insn
Pre-decode
Fetch Stage
Branch Type
IMM16/26
Target Address Pre-calculation
Branch Target
Target Selection
Next PC
Impractical on ASIC
Other possible targets

## Slide 13: Target Address Pre-calculation
Full Address Calculation (FAC): IMM26/IMM16
Partial Address Calculation (PAC): IMM16 only
I-Type
J-Type
insn
Pre-decode
Branch Type
IMM16/26

## Slide 14: Eliminating the BTB
93% of all branches are direct branches
97% of indirect branches are returns
Chart: 
| bzip2 | xalanc | average
Direct Branch | 0.99049 | 0.83985 | 0.93074
Indirect Branch | 0.0095145 | 0.16015 | 0.069259
Chart: 
| libquantum | sjeng | average
Return | 0.99925 | 0.62693 | 0.96908
Other indirect branches | 0.00075415 | 0.37307 | 0.030923

## Slide 15: Target Prediction Accuracy
Chart: Reduction in target address misprediction over Base
| BTB-256 | BTB-512 | BTB-1024 | BTB-PAC | BTB-FAC | FAC | FAC+RAS | BTB-1024 +RAS +FAC
 | 0.3032 | 0.2981 | 0.2938 | 0.8071 | 0.9016 | 0.8447 | 0.9356 | 0.98589
BTB+FAC+RAS has little target prediction accuracy improvement over FAC+RAS

## Slide 16: Road Map
Introduction
Branch Prediction Overview
Branch Target Predictors
Branch Direction Predictors
Conclusion

## Slide 17: Branch Direction Predictors
Altera’s Nios II-f only uses one BRAM for branch prediction
Two prone approach:
  A minimalistic branch predictor that also uses one BRAM
  No resource restrictions

## Slide 18: The Minimalistic Branch Predictor
Chart: Maximum Frequency (MHz)
| Base | BTB+ bimodal | FAC+RAS+ bimodal | FAC+RAS+ gselect | FAC+RAS+ gshare | FAC+RAS+ gRselect
fmax avg | 353.42 | 287.11 | 252.03 | 241.37 | 232.65 | 259.61
dumP | 0 | 0 | 0 | 0 | 0 | 0
dumS | 0 | 0 | 0 | 0 | 0 | 0
IPC | 0.2904 | 0.3031 | 0.322 | 0.3266 | 0.3285 | 0.3255
Fastest
Inaccurate
Slow
Accurate
Slowest
Most accurate
Slower
Very accurate
Fast
Very Accurate
Faster
Less inaccurate

## Slide 19: Timing details of gshare/gselect
GHR
…
f
Selection Logic
…
Target
Predictor/
Calculator
Predicted PC
DIR table

## Slide 20: gRselect
GHR
Selection Logic
…
Target
Predictor/
Calculator
Predicted PC
gRselect
16 DIR entries
32
2
…
PC

## Slide 21: Relaxing Storage Constraint
Chart: MPKI
| 1KB | 2KB | 4KB | 8KB | 16KB | 32KB
GRselect | 12.6754 | 11.9638 | 11.425 | 10.6605 | 10.4094 | 9.8396
GShare | 12.1582 | 11.3308 | 10.7309 | 10.3986 | 10.1152 | 9.8456
Bimodal | 19.0368 | 16.4073 | 16.1899 | 15.9806 | 15.837 | 15.6352
Accuracy saturates with increasing predictor sizes
Consider more advanced branch prediction schemes

## Slide 22: “Multiplication”
Weight Table
w1
……
negate
-w1
h1
negate
-wn
hn
wn
(a)
Weight Table
w1
……
-w1
h1
-wn
hn
wn
(b)
Complement Weight Table

## Slide 23: Low Order Bit Elimination
Chart: HOB
| 8 | 7 | 6 | 5 | 4 | 3 | 2 | 1
MPKI | 12.6266 | 12.4287 | 12.2479 | 12.6502 | 12.7707 | 12.7512 | 25.3793 | 61.2915
Using 3 bits at prediction time improves maximum frequency by 14.6% with negligible accuracy reduction

## Slide 24: Perceptron Predictor Structure on FPGA
Weight Table
……
Complement Weight Table
Wallace Tree
Replace a layer of adders with muxes

## Slide 25: Perceptron Predictor Structure on FPGA
6-LUT
Weight Table
……
Complement Weight Table
6-LUT
Wallace Tree
Reduces one layer of logic

## Slide 26: Overriding TAGE
The Statistical Corrector Improves Accuracy by ~2.4x
Fetch
Base Prediction
Decode
TAGE
Override
!=
Statistical Corrector

## Slide 27: Evaluation – Minimalistic Predictor
Baseline predictor
  256-entry fused BTB and bimodal
  Does not decode instructions, uses the BTB and the bimodal for all instructions
Data gathered from SPECCPU2006 benchmarks
Metrics | Description
Misses Per Kilo Instructions (MPKI) | Predictor accuracy
Target prediction rate | Target predictor accuracy
Instruction Per Cycle (IPC) | Overall branch predictor performance without considering maximum frequency
Million Instruction Per Second (MIPS) | Overall branch predictor performance

## Slide 28: Direction Prediction Schemes
gshare is the most accurate, followed by gselect and gRselect
Chart: MPKI improvement over baseline
| bimodal-4096 | gshare-4096 | gselect-4096 | gRselect-4096
 | 0.25 | 0.82 | 0.8 | 0.79

## Slide 29: Target Address Prediction Schemes
Chart: Reduction in mis-predicted target
| BTB-256 | BTB+FAC | FAC+RAS
 | 0.30324 | 0.90162 | 0.93563
FAC+RAS is the most accurate

## Slide 30: Maximum Frequency and Area
Chart: Maximum Frequency (MHz)
| Base | BTB+bimodal | BTB+PAC+bimodal | BTB+FAC+bimodal | FAC+RAS+bimodal | FAC+RAS+gshare | FAC+RAS+gselect | FAC+RAS+gRselect | FAC+RAS+gRselect+PD
fmax avg | 353.42 | 287.11 | 265.52 | 262.26 | 252.03 | 232.65 | 241.37 | 243.13 | 259.61
dumP | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
dumS | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
area avg | 46 | 50 | 108 | 107.6 | 141.6 | 154.4 | 142.6 | 151.4 | 147.8
FAC+RAS with gRselect+PD is faster than FAC+RAS with bimodal

## Slide 31: IPC and MIPS
Chart: IPC normalized to base
| Base | BTB+bimodal | FAC+RAS+bimodal | FAC+RAS+gshare | FAC+RAS+gRselect
Normalized IPC | 1 | 1.0234 | 1.0987 | 1.1172 | 1.1122
dumP | 0 | 0 | 0 | 0 | 0
dumS | 0 | 0 | 0 | 0 | 0
MIPS | 78.4009 | 81.8446 | 81.132 | 76.2036 | 84.9185
The overall best performing prediction scheme is FAC+RAS w/ gRselect

## Slide 32: Evaluation – Perceptron and TAGE
Bimodal, gshare and gRselect are scaled from 1KB to 32KB
All the schemes use FAC+RAS as target predictor
Four TAGE variations:
  single-cycle TAGE, single-cycle TAGE-SC, O-TAGE, O-TAGE-SC
Same methodology

## Slide 33: Accuracy
Chart: MPKI
| GRselect | GShare | Bimodal | Perceptron | Single-cycle TAGE | O-TAGE | Single-cycle TAGE-SC | O-TAGE-SC
1KB | 12.6754 | 12.1582 | 19.0368 | 17.3685
2KB | 11.9638 | 11.3308 | 16.4073 | 15.7182
4KB | 11.425 | 10.7309 | 16.1899 | 13.7762
8KB | 10.6605 | 10.3986 | 15.9806 | 13.1859
16KB | 10.4094 | 10.1152 | 15.837 | 12.6266
32KB | 9.8396 | 9.8456 | 15.6352 | 12.2322 | 10.1499 | 10.1544 | 4.2554 | 4.2527
TAGE-SC variations are ~2.3x more accurate than the best gRselect and gshare

## Slide 34: IPC
Chart: IPC
| GRselect | Gshare | Bimodal | Perceptron | Single-cycle TAGE | O-TAGE | Single-cycle TAGE-SC | O-TAGE-SC
1KB | 0.3255 | 0.3269 | 0.3236 | 0.3227
2KB | 0.3259 | 0.3276 | 0.3245 | 0.3237
4KB | 0.3264 | 0.328 | 0.3247 | 0.3251
8KB | 0.3269 | 0.3283 | 0.3248 | 0.3262
16KB | 0.3272 | 0.3284 | 0.3248 | 0.3272
32KB | 0.3276 | 0.3286 | 0.325 | 0.3272 | 0.3296 | 0.32669 | 0.33104 | 0.32942
O-TAGE-SC is within 0.5% of the single-cycle TAGE-SC

## Slide 35: Maximum Frequency
Chart: FMax (MHz)
| GRselect | GShare | Bimodal | Perceptron | Single-cycle TAGE | O-TAGE | Single-cycle TAGE-SC | O-TAGE-SC
1KB | 259.6 | 238.3 | 252 | 262.482
2KB | 258.3 | 235.7 | 243.5 | 235.842
4KB | 255 | 228.4 | 234.9 | 227.55
8KB | 254.2 | 219.6 | 229.7 | 213.74
16KB | 255.8 | 217.9 | 217.2 | 206.972
32KB | 248.948 | 197.112 | 200.992 | 165.018 | 221.874 | 270 | 223.664 | 270
O-TAGE variations are capped at 270 MHz

## Slide 36: IPS
Chart: Million Instructions Per Second
| GRselect | Gshare | Bimodal | Perceptron | Single-cycle TAGE-SC | O-TAGE-SC
1KB | 84.4998 | 77.9003 | 81.5472 | 84.7029
2KB | 84.18 | 77.2153 | 79.0157 | 76.3421
4KB | 83.232 | 74.9152 | 76.272 | 73.9765
8KB | 83.098 | 72.0947 | 74.6066 | 69.722
16KB | 83.6978 | 71.5584 | 70.5466 | 67.7212
32KB | 81.5554 | 64.771 | 65.3224 | 53.9939 | 74.0417 | 88.9434
O-TAGE-SC delivers 5.2% higher IPS than the 1KB gRselect

## Slide 37: Conclusion
The best performing minimalistic branch predictor is FAC+RAS with gRselect
TAGE is best used as an overriding predictor, and O-TAGE-SC is 5.2% better than the best gRselect.

## Slide 38: Thank you!
Questions?

## Slide 39: Backup Slides

## Slide 40: FAC+RAS with gRselect
PC
GHR
iCache
16, 2-bit sat. counters
gRselect
32
2
…
Target Predictor/
Calculator
+4
Predicted PC
Selection Logic

## Slide 41: Direction Predictors: MPKI improvement over Base

## Slide 42: Reduction in target address mis-prediction over BASE

## Slide 43: List of Benchmarks
bzip2
gobmk
hmmer
sjeng
libquantum
h264
astar
xalanc