## Slide 1: High-performance Branch Predictors For Soft Processors
Di Wu
M.A.Sc Defense
September 8, 2014

## Slide 2: Why Branch Prediction
Fetch and execute speculatively
Without a Branch Predictor
stall
Branch Predictor: Correct prediction
Fetch and execute speculatively
Branch Predictor: Incorrect prediction
Branch resolved
Squash
Guess Next PC
Guess Next PC
Branch
Time

## Slide 3: Branch Predictors on FPGAs
iCache
(BRAM)
Branch Prediction Table
(BRAM)
Branch Prediction Logic
Fetch Stage
Decode Stage
Next PC
Faster relative to ASIC
Slower relative to ASIC

## Slide 4: Proposed Branch Predictor
Frequency | 259 MHz
Instruction per cycle (IPC) | 0.3266
Million instructions per second (MIPS) | 84.92
Area (# ALUTs) | 147
# M9K BRAM | 1

## Slide 5: Road Map
Introduction
Goals
Branch Prediction Overview
FPGA implementation
Evaluation
Conclusion

## Slide 6: Goals
A branch predictor for soft-processors that:
  Balance operating frequency and accuracy
  Uses as few on-chip resources as possible

## Slide 7: Branch Prediction
iCache
Branch Prediction
Table
Branch Prediction Logic
Fetch Stage
Decode Stage
Next PC
REQ1: Guess the direction of a branch
REQ2: Guess its target (Next PC)
Fetch instructions from there
Execute Speculatively
Verify if the prediction was correct

## Slide 8: REQ #1. Direction Predictor
PC
…
bimodal
PC
…
gshare
GHR
XOR
PC
…
gselect
Concatenate
DIR table
DIR table
DIR table
GHR

## Slide 9: REQ #2. Target Predictor
Branch Target Buffer (BTB)
  Can be used for all branches
Return Address Stack (RAS)
  Uses calls to predict targets of returns
Target Address Pre-calculation

## Slide 10: Canonical Branch Predictor
PC
BTB
+4
PC + 4
DIR
Next PC
RAS
Selection Logic

## Slide 11: Target Address Pre-calculation
iCache
insn
Pre-decode
Fetch Stage
Branch Type
IMM16/26
Target Address Pre-calculation
Branch Target
Target Selection
Next PC
Impractical on ASIC
Other possible targets

## Slide 12: Target Address Pre-calculation
Full Address Calculation (FAC): IMM26/IMM16
Partial Address Calculation (PAC): IMM16 only
I-Type
J-Type
insn
Pre-decode
Branch Type
IMM16/26

## Slide 13: Fused BTB and bimodal
256
30
2
……
……
Branch Targets
2
2
……
……
Directions
Index
Stratix IV M9K BRAM

## Slide 14: BRAM configurations
PC[9:2]
BTB + bimodal-256
256
BTB + bimodal-768
256
PC[9:2]
PC
BTB + gshare
256
PC GHR
Cannot access both in the same cycle
PC[11:10]
BTB + gselect-768
256
PC[9:2]
GHR[1:0]

## Slide 15: Eliminating the BTB
93% of all branches are direct branches
97% of indirect branches are returns
Chart: 
| bzip2 | xalanc | average
Direct Branch | 0.99049 | 0.83985 | 0.93074
Indirect Branch | 0.0095145 | 0.16015 | 0.069259
Chart: 
| libquantum | sjeng | average
Return | 0.99925 | 0.62693 | 0.96908
Other indirect branches | 0.00075415 | 0.37307 | 0.030923

## Slide 16: Eliminating the BTB
FAC
RAS
Target Predictor
The BRAM can be dedicated to direction prediction
Branch Type
IMM16/26
BTB
Index
BRAM

## Slide 17: Timing details of gshare/gselect
GHR
…
f
Selection Logic
…
Target
Predictor/
Calculator
Predicted PC
DIR table

## Slide 18: gRselect
GHR
Selection Logic
…
Target
Predictor/
Calculator
Predicted PC
gRselect
16 DIR entries
32
2
…
PC

## Slide 19: Evaluation
Baseline predictor
  256-entry fused BTB and bimodal
  Does not decode instructions, uses the BTB and the bimodal for all instructions
Data gathered from SPECCPU2006 benchmarks
Metrics | Description
Misses Per Kilo Instructions (MPKI) | Predictor accuracy
Target prediction rate | Target predictor accuracy
Instruction Per Cycle (IPC) | Overall branch predictor performance without considering maximum frequency
Million Instruction Per Second (MIPS) | Overall branch predictor performance

## Slide 20: Direction Prediction Schemes
gshare is the most accurate, followed by gselect and gRselect
Chart: MPKI improvement over baseline
| bimodal-4096 | gshare-4096 | gselect-4096 | gRselect-4096
 | 0.25 | 0.82 | 0.8 | 0.79

## Slide 21: Target Address Prediction Schemes
Chart: Reduction in mis-predicted target
| BTB-256 | BTB+FAC | FAC+RAS
 | 0.30324 | 0.90162 | 0.93563
FAC+RAS is the most accurate

## Slide 22: Maximum Frequency and Area
Chart: Maximum Frequency (MHz)
| Base | BTB+bimodal | BTB+PAC+bimodal | BTB+FAC+bimodal | FAC+RAS+bimodal | FAC+RAS+gshare | FAC+RAS+gselect | FAC+RAS+gRselect | FAC+RAS+gRselect+PD
fmax avg | 353.42 | 287.11 | 265.52 | 262.26 | 252.03 | 232.65 | 241.37 | 243.13 | 259.61
dumP | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
dumS | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
area avg | 46 | 50 | 108 | 107.6 | 141.6 | 154.4 | 142.6 | 151.4 | 147.8
FAC+RAS with gRselect+PD is faster than FAC+RAS with bimodal

## Slide 23: IPC and MIPS
Chart: IPC normalized to base
| Base | BTB+bimodal | FAC+RAS+bimodal | FAC+RAS+gshare | FAC+RAS+gRselect
Normalized IPC | 1 | 1.0234 | 1.0987 | 1.1172 | 1.1122
dumP | 0 | 0 | 0 | 0 | 0
dumS | 0 | 0 | 0 | 0 | 0
MIPS | 78.4009 | 81.8446 | 81.132 | 76.2036 | 84.9185
The overall best performing prediction scheme is FAC+RAS w/ gRselect

## Slide 24: Conclusion
The best performing branch predictor is FAC+RAS with gRselect
  Operates at 259 MHz
  Uses 147 ALUTs and 1 M9K BRAM
  Delivers 84.9 Million instructions per second over SPECCPU2006 benchmarks

## Slide 25: Thank you!
Questions?

## Slide 26: Backup Slides

## Slide 27: FAC+RAS with gRselect
PC
GHR
iCache
16, 2-bit sat. counters
gRselect
32
2
…
Target Predictor/
Calculator
+4
Predicted PC
Selection Logic

## Slide 28: Direction Predictors: MPKI improvement over Base

## Slide 29: Reduction in target address mis-prediction over BASE

## Slide 30: List of Benchmarks
bzip2
gobmk
hmmer
sjeng
libquantum
h264
astar
xalanc