## Slide 1: High-Performance Branch Predictors For Soft Processors
Di Wu
M.A.Sc. Defense
September 8, 2014

## Slide 2: Why Branch Prediction
Fetch and execute speculatively
Without a Branch Predictor
stall
Branch Predictor: Correct prediction
Fetch and execute speculatively
Branch Predictor: Incorrect prediction
Branch resolved
Squash
Guess Next PC
Guess Next PC
Branch
Time
Notes: Wrong prediction: penalty to squash

## Slide 3: Branch Predictors on FPGAs
iCache
(BRAM)
Branch Prediction Table
(BRAM)
Branch Prediction Logic
Fetch Stage
Decode Stage
Next PC
Faster relative to ASIC
Slower relative to ASIC
Notes: The latency gap between accessing on-chip memory and logic is much smaller relative to ASIC.
Need to re-evaluate tradeoffs.
This work proposes FPGA-friendly branch predictors

## Slide 4: This Work
Chart: Fmax (MHz)
| 259.60000000000002 | 258.3 | 255 | 254.2 | 255.8 | 248.94800000000001 | 238.3 | 235.7 | 228.4 | 219.6 | 217.9 | 197.11199999999999 | 252 | 243.5 | 234.9 | 229.7 | 217.2 | 200.99199999999999 | 262.48200000000003 | 235.84200000000001 | 227.55 | 213.74 | 206.97200000000001 | 165.018 | 221.874 | 270 | 223.66399999999999 | 270
 | 12.6754 | 11.9638 | 11.425 | 10.6605 | 10.4094 | 9.8396 | 12.1582 | 11.3308 | 10.7309 | 10.3986 | 10.1152 | 9.8456 | 19.0368 | 16.4073 | 16.1899 | 15.9806 | 15.837 | 15.6352 | 17.3685 | 15.7182 | 13.7762 | 13.1859 | 12.6266 | 12.2322 | 10.1499 | 10.1544 | 4.2554 | 4.2527
1KB gRselect
O-TAGE-SC
better
1KB Perceptron
Notes: Points: designs
Vertical axis: MPKI, horizontal axis: Fmax
Contribution: Propose O-TAGE-SC and gRselect

## Slide 5: Road Map
Introduction
Branch Prediction Overview
Branch Target Predictors
Branch Direction Predictors
Conclusion

## Slide 6: Branch Prediction Overview
iCache
Branch Prediction
Table
Branch Prediction Logic
Fetch Stage
Decode Stage
Next PC
REQ1: Guess the direction of a branch
REQ2: Guess its target (Next PC)
Fetch instructions from there
Execute Speculatively
Verify if the prediction was correct
Notes: Goal: provide next pc
5 steps

## Slide 7: REQ #1. Direction Prediction
PC
…
bimodal
PC
…
gshare
GHR
XOR
PC
…
gselect
Concatenate
DIR table
DIR table
DIR table
GHR
Correlation with preceding branch outcomes
Temporal bias
Notes: All have DIR table, indexing is different
Bimodal captures temporal bias: no correlation between branches
Gshare and Gselect uses GHR, which stores preceding branch results, to finds correlations between branch outcomes and global branch history patterns
Gshare XOR while Gselect concatenate

## Slide 8: Direction Prediction: Perceptron
weight vector
Weight Table
w0
X
G0
wh
X
Gh
……
+
Correlation with relevant preceding branch outcomes
Notes: How it works: Perceptron uses weight vectors to represent correlations
Idea: a branch may not necessarily correlate with all previous branches
Branches that are not correlated will contribute little to the prediction

## Slide 9: Direction Prediction: TAGE
T1
hit?
T2
hit?
T3
hit?
T4
hit?
Prediction
How far back should we look for correlations?
Hist
Hist
Hist
Hist
T0
Notes: Use different history length to determine how far back should we look for correlations
Most accurate but requires many tables

## Slide 10: REQ #2: Target Predictor
Branch Target Buffer (BTB)
  Can be used for all branches
Return Address Stack (RAS)
  Uses calls to predict targets of returns
Target Address Pre-calculation
  Calculate address after fetching, FPGA-specific
Notes: We propose target address pre-calculation, specifically for soft-processors

## Slide 11: ASIC-like Branch Predictor for Nios II
PC
BTB
+4
PC + 4
DIR
RAS
Selection Logic
REQ#2: Target
REQ#1: Direction
Next PC
Notes: Will show this structure is not good on FPGA

## Slide 12: Road Map
Introduction
Branch Prediction Overview
Branch Target Predictors
Branch Direction Predictors
Conclusion

## Slide 13: Target Address Pre-calculation
PC
BTB
+4
PC + 4
DIR
Next PC
RAS
Selection Logic
insn
Pre-decode
Branch Type
Target Address Pre-calcuation
IMM16/26
Full Address Calculation (FAC): IMM26/IMM16
Partial Address Calculation (PAC): IMM16 only
Target Predictor
Notes: Discovered that it’s better to replace the BTB and with address calculation
Impractical on ASIC, 3 Cycles to access iCache, won’t even see insn in 1 cycel.

## Slide 14: Eliminating the BTB
93% of all branches are direct branches
97% of indirect branches are returns
Chart: 
| bzip2 | xalanc | average
Direct Branch | 0.99049 | 0.83985 | 0.93074
Indirect Branch | 0.0095145 | 0.16015 | 0.069259
Chart: 
| libquantum | sjeng | average
Return | 0.99925 | 0.62693 | 0.96908
Other indirect branches | 0.00075415 | 0.37307 | 0.030923
best
worst
overall
best
worst
overall
FAC+RAS: cover over 99% of all branches
Notes: Vertical axis: percentage of instructions, horizontal axis: benchmarks, best worst average
Eliminate BTB -> lose coverage
Studied histogram to show the impact is minimal

## Slide 15: We don’t need a BTB
BTB+FAC+RAS vs. FAC+RAS: ~5% target accuracy improvement
But direction accuracy suffers
Chart: Reduction in Target Address Misprediction over Base.
| FAC | BTB+FAC | FAC+RAS | BTB+FAC+RAS
 | 0.8447 | 0.9016 | 0.9356 | 0.98589
Notes: Vertical axis: percentage improvement, horizontal axis: target predictors
FAC+RAS is better than BTB+FAC
Including BTB+FAC+RAS only improves ~5% -> little impact on target accuracy, so use FAC+RAS

## Slide 16: Road Map
Introduction
Branch Prediction Overview
Branch Target Predictors
Branch Direction Predictors
Conclusion

## Slide 17: Branch Direction Predictors
Altera’s Nios II-f branch predictor: one BRAM
  Balances area vs. performance?
Two approaches:
  Minimalistic: One BRAM
  Unrestricted: as many as justified

## Slide 18: Minimalistic: Gshare/Gselect Critical Path
GHR
…
f
Selection Logic
…
Target
Predictor/
Calculator
Predicted PC
DIR table
Notes: Straight forward implementation of gshare and gselect is slow

## Slide 19: gRselect: Breaking the Critical Path
GHR
Selection Logic
…
Target
Predictor/
Calculator
Predicted PC
gRselect
16 DIR entries
32
2
…
PC

## Slide 20: Minimalistic: Fmax vs. IPC
Chart: Maximum Frequency (MHz)
| Base | FAC+RAS+ bimodal | FAC+RAS+ gselect | FAC+RAS+ gshare | FAC+RAS+ gRselect
Fmax | 353.42 | 252.03 | 241.37 | 232.65 | 259.61
dumP | 0 | 0 | 0 | 0 | 0
dumS | 0 | 0 | 0 | 0 | 0
IPC | 0.2904 | 0.322 | 0.3266 | 0.3285 | 0.3255
Fast
Inaccurate
Slowest
Most accurate
Slow
Very accurate
Fast
Very Accurate
slow
Accurate
Slower
More Accurate
Notes: Vertical axis: fmax and IPC, horizontal axis: various predictors
Base is fast but capped at 270MHz

## Slide 21: IPC and IPS
Chart: IPC normalized to base
| Base | BTB+bimodal | FAC+RAS+bimodal | FAC+RAS+gshare | FAC+RAS+gRselect
Normalized IPC | 1 | 1.0234 | 1.0987 | 1.1172 | 1.1122
dumP | 0 | 0 | 0 | 0 | 0
dumS | 0 | 0 | 0 | 0 | 0
MIPS | 78.4009 | 81.8446 | 81.132 | 76.2036 | 84.9185
FAC+RAS w/ gRselect is best
Notes: Vertical axis: IPC normalized to base, MIPS, horizontal axis: predictors
MIPS on the same ISA, so it’s OK

## Slide 22: Fmax sensitivity
Chart: Processor Operating Frequency
| 220 | 230 | 240 | 250 | 260 | 270 | 280 | 290 | 300 | 310 | 320 | 330 | 340 | 350 | 360 | 370
Base | 63.888 | 66.792 | 69.696 | 72.6 | 75.504 | 78.408 | 81.312 | 84.216 | 87.12 | 90.024 | 92.928 | 95.832 | 98.736 | 101.64 | 102.6332 | 102.6332
FAC+RAS+ bimodal | 70.84 | 74.06 | 77.28 | 80.5 | 81.1537 | 81.1537 | 81.1537 | 81.1537 | 81.1537 | 81.1537 | 81.1537 | 81.1537 | 81.1537 | 81.1537 | 81.1537 | 81.1537
FAC+RAS+ gselect | 71.852 | 75.118 | 78.384 | 78.8314 | 78.8314 | 78.8314 | 78.8314 | 78.8314 | 78.8314 | 78.8314 | 78.8314 | 78.8314 | 78.8314 | 78.8314 | 78.8314 | 78.8314
FAC+RAS+ gshare | 72.27 | 75.555 | 76.4255 | 76.4255 | 76.4255 | 76.4255 | 76.4255 | 76.4255 | 76.4255 | 76.4255 | 76.4255 | 76.4255 | 76.4255 | 76.4255 | 76.4255 | 76.4255
FAC+RAS+ gRselect | 71.61 | 74.865 | 78.12 | 81.375 | 84.5031 | 84.5031 | 84.5031 | 84.5031 | 84.5031 | 84.5031 | 84.5031 | 84.5031 | 84.5031 | 84.5031 | 84.5031 | 84.5031
Base outperforms FAC+RAS+gRselect when the processor runs above 293MHz
Notes: In this study, the fmax of Base is capped at 270MHz.
Processor faster -> Base can improve while the other predictors stay the same
Vertical axis: IPS, horizontal axis: fmax of the processor
When the processor operates at 293MHz or faster, Base outperforms FAC+RAS+gRselect

## Slide 23: Relaxing the Storage Constraint
Chart: MPKI
| 1KB | 2KB | 4KB | 8KB | 16KB | 32KB
GRselect | 12.6754 | 11.9638 | 11.425 | 10.6605 | 10.4094 | 9.8396
GShare | 12.1582 | 11.3308 | 10.7309 | 10.3986 | 10.1152 | 9.8456
Bimodal | 19.0368 | 16.4073 | 16.1899 | 15.9806 | 15.837 | 15.6352
Accuracy saturates with increasing predictor sizes
Consider more advanced branch prediction schemes
Notes: Vertical axis: MPKI, horizontal axis: predictor sizes

## Slide 24: Perceptron
Optimizations to improve maximum frequency
  Complement table
  Low Order Bit (LOB) elimination
  Weight arrangement
  Wallace tree
Overall 17.5% faster than the naïve implementation
Still not the best

## Slide 25: Single Cycle TAGE
Fetch
Single-Cycle TAGE
Decode
Next PC
iCache
Original TAGE by Seznec
Too slow

## Slide 26: Overriding TAGE
iCache
Fetch
Decode
T0
Tagged Componets
!=
O-TAGE
Override
Next PC
Overrides too frequently
  Correct override: gain one cycle vs. mispredicting
  Incorrect override: lose two cycles
Need to be careful with overrides

## Slide 27: Overriding TAGE + Statistical Corrector
iCache
Fetch
Decode
T0
Tagged Componets
O-TAGE-SC
Override
Next PC
Statistical Corrector
Statistical Corrector
  Table: maps well onto BRAM
  Saturating counters: 10-bit wide
    Must see 1K correct overrides before overriding
    Reset on incorrect override

## Slide 28: Accuracy vs. Predictor Size
Chart: MPKI
| GRselect | GShare | Bimodal | Perceptron | Single-cycle TAGE | O-TAGE | Single-cycle TAGE-SC | O-TAGE-SC
1KB | 12.6754 | 12.1582 | 19.0368 | 17.3685
2KB | 11.9638 | 11.3308 | 16.4073 | 15.7182
4KB | 11.425 | 10.7309 | 16.1899 | 13.7762
8KB | 10.6605 | 10.3986 | 15.9806 | 13.1859
16KB | 10.4094 | 10.1152 | 15.837 | 12.6266
32KB | 9.8396 | 9.8456 | 15.6352 | 12.2322 | 10.1499 | 10.1544 | 4.2554 | 4.2527
TAGE-SC variations are ~2.3x more accurate than the best gRselect and gshare
Notes: Vertical axis: MPKI, horizontal axis: predictors
All predictors gets more accurate as they scale
TAGE-SC variations are 2.3x more accurate than the 32KB gshare

## Slide 29: Fmax
Chart: FMax (MHz)
| GRselect | GShare | Bimodal | Perceptron | Single-cycle TAGE | O-TAGE | Single-cycle TAGE-SC | O-TAGE-SC
1KB | 259.6 | 238.3 | 252 | 262.482
2KB | 258.3 | 235.7 | 243.5 | 235.842
4KB | 255 | 228.4 | 234.9 | 227.55
8KB | 254.2 | 219.6 | 229.7 | 213.74
16KB | 255.8 | 217.9 | 217.2 | 206.972
32KB | 248.948 | 197.112 | 200.992 | 165.018 | 221.874 | 270 | 223.664 | 270
O-TAGE variations are capped at 270 MHz
Notes: Vertical axis: fmax, horizontal axis: predictors
O-TAGE-SC is capped at 270MHz
Other predictors slows down as they scale, gRselect suffers less because of its critical path is different

## Slide 30: IPS
Chart: Million Instructions Per Second
| GRselect | Gshare | Bimodal | Perceptron | Single-cycle TAGE-SC | O-TAGE-SC
1KB | 84.4998 | 77.9003 | 81.5472 | 84.7029
2KB | 84.18 | 77.2153 | 79.0157 | 76.3421
4KB | 83.232 | 74.9152 | 76.272 | 73.9765
8KB | 83.098 | 72.0947 | 74.6066 | 69.722
16KB | 83.6978 | 71.5584 | 70.5466 | 67.7212
32KB | 81.5554 | 64.771 | 65.3224 | 53.9939 | 74.0417 | 88.9434
O-TAGE-SC delivers 5.2% higher IPS than the 1KB gRselect
Notes: Vertical axis: IPS
O-TAGE-SC is the best because it’s both the fastest and the most accurate
Followed by 1KB perceptron and 1KB Grselect
Single-cycle TAGE-SC is too slow

## Slide 31: IPS Improvement Over 1KB Gshare Breakdown
Chart: 
| gRselect | Perceptron | O-TAGE-SC
Fmax | 0.11588 | 0.12823 | 0.16054
IPC | -0.0091324 | -0.017656 | 0.0028006
Notes: Vertical axis: IPS improvement
Blue bar: contribution from fmax, red bar: contribution from IPC
The major IPS gain comes from fmax.
Even O-TAGE-SC is 2.3x more accurate, it’s only 0.3% better in IPC, most because of the small pipeline so the ultimate gain is limited

## Slide 32: Conclusion
The best performing minimalistic branch predictor is FAC+RAS with gRselect
TAGE is best used as an overriding predictor, and O-TAGE-SC is 5.2% better than the best gRselect.

## Slide 33: Publications
Di Wu, Kaveh Aasaraai and Andreas Moshovos, "Low-cost, High-performance Branch Predictors for Soft Processors", FPL’13
Di Wu and Andreas Moshovos, "Image Signal Processors for FPGAs“ (poster), FCCM’14
Goran Narancic, Patrick Judd, Di Wu, Islam Atta, Michel El Nacouzi, Jason Zebchuk, Natalie Enright Jerger, Serag Gadelrab, Kyros Kutulakos, Andreas Moshovos and Jorge Albericio. “Evaluating Memory System Behavior of SmartphoneWorkloads.” SAMOS'14
Di Wu and Andreas Moshovos, “Advanced Branch Predictors for Soft Processors”, submitted to ReConfig’14

## Slide 34: Thank you!
Questions?

## Slide 35: Backup Slides

## Slide 36: FAC+RAS with gRselect
PC
GHR
iCache
16, 2-bit sat. counters
gRselect
32
2
…
Target Predictor/
Calculator
+4
Predicted PC
Selection Logic

## Slide 37: “Multiplication”
Weight Table
w1
……
negate
-w1
h1
negate
-wn
hn
wn
(a)
Weight Table
w1
……
-w1
h1
-wn
hn
wn
(b)
Complement Weight Table

## Slide 38: Low Order Bit Elimination
Chart: HOB
| 8 | 7 | 6 | 5 | 4 | 3 | 2 | 1
MPKI | 12.6266 | 12.4287 | 12.2479 | 12.6502 | 12.7707 | 12.7512 | 25.3793 | 61.2915
Using 3 bits at prediction time improves maximum frequency by 14.6% with negligible accuracy reduction

## Slide 39: Perceptron Predictor Structure on FPGA
Weight Table
……
Complement Weight Table
Wallace Tree
Replace a layer of adders with muxes

## Slide 40: Perceptron Predictor Structure on FPGA
6-LUT
Weight Table
……
Complement Weight Table
6-LUT
Wallace Tree
Reduces one layer of logic

## Slide 41: IPC
Chart: IPC
| GRselect | Gshare | Bimodal | Perceptron | Single-cycle TAGE | O-TAGE | Single-cycle TAGE-SC | O-TAGE-SC
1KB | 0.3255 | 0.3269 | 0.3236 | 0.3227
2KB | 0.3259 | 0.3276 | 0.3245 | 0.3237
4KB | 0.3264 | 0.328 | 0.3247 | 0.3251
8KB | 0.3269 | 0.3283 | 0.3248 | 0.3262
16KB | 0.3272 | 0.3284 | 0.3248 | 0.3272
32KB | 0.3276 | 0.3286 | 0.325 | 0.3272 | 0.3296 | 0.32669 | 0.33104 | 0.32942
O-TAGE-SC is within 0.5% of the single-cycle TAGE-SC

## Slide 42: List of Benchmarks
bzip2
gobmk
hmmer
sjeng
libquantum
h264
astar
xalanc